## Slide 1
The Great South Bay and the New Inlet
Bellport Middle School, Dec 21, 2013
Charles Flagg, Roger Flood, Robert Wilson and Dong-Ming Yang
Pilots: Rich Giannotti, Charles Flagg, Don Richards & Vinny Petruso
Photographers: Charles Flagg, Rich Weissman, Mike Ferrigno,
Justin Flagg, Brian Wasser, Jamie Shreeve, John Vahey,
Brad Furman, Chris Gobler and Mike Busch
http://po.msrc.sunysb.edu/GSB

## Slide 2
Topics
  The breach and the evolution of the New Inlet
  Bathymetric and Velocity Survey Results
  Salinity and Changes in Bay-Ocean Exchange

## Slide 3
76 km
E. Rockaway
Jones
Fire Island
Moriches
The Great South Bay
New Inlet
Notes: Amityville

## Slide 4
Aerial Photography

## Slide 5
April 9, 2005
C. Flagg
Notes: 5
5

## Slide 6
November 3, 2012 ~0900 EDT (~1300 GMT)
C. Flagg and R. Giannotti
Notes: 6
6

## Slide 7
Nov 11
Nov 29
Jan 6
Nov 3
Nov 11
Nov 18
Dec 20
Feb 14

## Slide 8
Sept 15, 2013 Flight Track

## Slide 9
Google Earth KML file
http://wx.somassbu.org/products/kml/OldInletBreach.kml
showing a series of aerial photo mosaics of the New Inlet

## Slide 10
Aerial Photos

## Slide 11
Bathymetric (Depth) Surveying

## Slide 12
Bathymetric Surveying

## Slide 13
Inlet Bottom Profiles Across the Deepest Section

## Slide 14
Inlet Bottom Profiles Across the Deepest Section

## Slide 15
Inlet Bottom Profiles Across the Deepest Section

## Slide 16
Inlet Bottom Profiles Across the Deepest Section

## Slide 17
Inlet Bottom Profiles Across the Deepest Section

## Slide 18
Inlet Bottom Profiles Across the Deepest Section

## Slide 19
Inlet Bottom Profiles Across the Deepest Section

## Slide 20
Inlet Bottom Profiles Across the Deepest Section

## Slide 21
Inlet Bottom Profiles Across the Deepest Section

## Slide 22
Inlet Bottom Profiles Across the Deepest Section

## Slide 23
Inlet Bottom Profiles Across the Deepest Section

## Slide 24
Inlet Bottom Profiles Across the Deepest Section
Latest Profile
Nov 6, 2013

## Slide 25
Area
New Inlet
~400 m2
Fire Island Inlet ~ 4000 m2
Moriches Inlet ~ 800 m2
Total ~ 4800 m2
New Inlet is ~ 8% of Total

## Slide 26
Velocity Survey of the Inlet, November 17, 2013
Acoustic Doppler Current Profiler (ADCP) mounted on a 14’ skiff.
1200 kHz RDI Workhorse ADCP

## Slide 27
Velocity Survey of the Inlet, November 17, 2013
Boat Track
70 round trips across main transect
from slack after high water to slack after low water.

## Slide 28
Velocity Survey of the Inlet, November 17, 2013
Maximum observed current: 2.2 m/s (4.7 kts)
Maximum ebb transport: 445 m3/s
Total ebb transport: 6.8 x 106 m3
1 m/s

## Slide 29
New
Inlet
Tidal range at Bellport on November 17 was 0.39 m, so the area directly affected by the transport through the inlet was
6.8 x 106 m3 /0.39 m = 17.6 km2.
This area is approximately the size of Bellport Bay and 8% of the larger Great South Bay.
GSB Area = 216 km2
Bellport Bay Area = 18 km2

## Slide 32
Salinities in Great South Bay by Station
Ocean
Bellport Bay

## Slide 33
Records from Bellport and the GSB1 Buoy show the effects of the increased ocean-bay exchange in Bellport Bay.

## Slide 34
Bellport
GSB Buoy
Sandy
FI Inlet
Dredging
9” Rain
Brown Tide
More
Dredging ?
Ocean ~31
Bellport
GSB Buoy

## Slide 35
Circulation within Great South Bay, Tides and Wind

## Slide 36
Wind Direction vs Bellport Water Level
Typical Nor’easter
or
Approaching Hurricane
Cold Outbreak
with Winds from
the northwest

## Slide 37
Woods Hole
Bellport
Lindehurst
Atlantic City
Chesapeake Bay
We have seen Wide Spread Sea Level Fluctuations

## Slide 39
Summary
The outer inlet has increased in size and moved west while the cross-sectional area has remained relatively stable for ~9 months.

## Slide 40
Summary
The outer inlet has increased in size and moved west while the cross-sectional area has remained relatively stable for ~9 months.
With the extended spit along the western edge, the inlet is continuing its rotation and growing longer, as happens with natural inlets.

## Slide 41
Summary
The outer inlet has increased in size and moved west while the cross-sectional area has remained relatively stable for ~9 months.
With the extended spit along the western edge, the inlet is continuing its rotation and growing longer, as happens with natural inlets.
The inlet is relatively small compared to the other inlets, < 8% of the cross-sectional areas with < 8% of the tidal exchange.

## Slide 42
Summary
The outer inlet has increased in size and moved west while the cross-sectional area has remained relatively stable for ~9 months.
With the extended spit along the western edge, the inlet is continuing its rotation and growing longer, as happens with natural inlets.
The inlet is relatively small compared to the other inlets, < 8% of the cross-sectional areas with < 8% of the tidal exchange.
There has been an increased exchange of waters with the ocean in the eastern Great South Bay, and this has clearly improved the water quality and reduced the impact of Brown Tides.

## Slide 43
Summary
The outer inlet has increased in size and moved west while the cross-sectional area has remained relatively stable for ~9 months.
With the extended spit along the western edge, the inlet is continuing its rotation and growing longer, as happens with natural inlets.
The inlet is relatively small compared to the other inlets, < 8% of the cross-sectional areas with < 8% of the tidal exchange.
There has been an increased exchange of waters with the ocean in the eastern Great South Bay, and this has clearly improved the water quality and reduced the impact of Brown Tides.
We experienced unusually frequent storms during last winter, which caused repeated local flooding events but these are not historically exceptional.

## Slide 44
Summary
The outer inlet has increased in size and moved west while the cross-sectional area has remained relatively stable for ~9 months.
With the extended spit along the western edge, the inlet is continuing its rotation and growing longer, as happens with natural inlets.
The inlet is relatively small compared to the other inlets, < 8% of the cross-sectional areas with < 8% of the tidal exchange.
There has been an increased exchange of waters with the ocean in the eastern Great South Bay, and this has clearly improved the water quality and reduced the impact of Brown Tides.
We experienced unusually frequent storms during last winter, which caused repeated local flooding events but these are not historically exceptional.
Bay waters will respond to storm-forced ocean surges, with or without the inlet.